## Slide 1
TOPIC A1:
COMPUTER FUNDAMENTALS
LESSON A1-5
LOGIC DIAGRAMS & TRUTH TABLES

## Slide 2
Guided Notes
ur hedz
Logic Gates
The seven operators
Truth tables – Circuits
Truth tables - descriptions
Boolean expressions and logic diagrams
Boolean algebra: simplifying
Karnaugh maps
WS A1-2: Diagram Double Down
WHAT U NEED 4 LESSON
AGENDA

## Slide 3
Last lesson everything was a number written in binary.
(a) Convert 1010 0110 to decimal.
(b) Convert the same byte to hexadecimal.
(c) State how many different values one nibble can represent.
-> Notes Q1 (a)-(c) [3 marks] - do them now
THE WARM UP QUESTION

## Slide 4
Last time, we looked at how to convert numbers to and from binary and hexadecimal
(a) Convert 1010 0110 to decimal.
(b) Convert the same byte to hexadecimal.
(c) State how many different values one nibble can represent.
-> Notes Q1 (a)-(c)
THE WARM UP QUESTION

## Slide 5
(a) 128 + 32 + 4 + 2 = 166
(b) 1010 = A, 0110 = 6, so A6
(c) Four bits, 2^4 = 16
THE WARM UP ANSWER

## Slide 6
Last time, we used 0 and 1 to store things, but this time, we’ll use them to decide things
Every conditional statement, like ifs and whiles, is a hardware question:
  Given these inputs, is the answer 1 or 0?
A logic gate is a physical circuit that answers one of those questions.
Millions of them wired together are what make up the ALU
TWO STATES, NOW DECISIONS

## Slide 7
One or two inputs, always one output
A Boolean operator is the check the gate applies.
  A gate takes that check and makes it out of transistors
A truth table lists every possible combination of inputs and the output for each
Two inputs means four rows. Three inputs means eight, so on and so forth, 2n
  Before you fill a truth table out, make sure you have the right number of rows
WHAT A GATE IS

## Slide 8
AND - output 1 only when both inputs are 1
OR - output 1 when at least one input is 1
NOT - one input, outputs the opposite
  Also called an inverter
AND, OR, NOT
A | B | A AND B | A OR B
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 1
A | NOT
0 | 1
1 | 0

## Slide 9
NAND - AND with the output flipped. Output 0 only when both inputs are 1
NOR - OR with the output flipped. Output 1 only when both inputs are 0
The symbol is the AND or OR shape with a small circle on the output, the circle representing the inversion
Every other gate can be built out of NAND alone, which is why you may have heard of NAND before
NAND, NOR
A | B | A NAND B | A NOR B
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0

## Slide 10
XOR - exclusive OR. Output 1 only when the inputs are different
XNOR - output 1 only when the inputs are the same. XOR inverted
XOR is a tricky one, so be sure to review that one especially
XOR, XNOR
A | B | A XOR B | A XNOR B
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 11
-> Notes Q2 [7 marks] - fill in all seven columns
If you can rebuild this table from scratch you should be pretty much clear for this part of the topic
THE SEVEN, ON YOUR NOTES

## Slide 12
A logic diagram is these gates wired together, with signals traveling from left to right
Solve gates with known inputs first, then use the results of those to determine future gates
When working through truth tables for logic diagrams, you should add intermediate columns for the middle work
  The IB tends to mark you up for having intermediate columns
READING A CIRCUIT

## Slide 13
Let’s say we have three inputs. A and B go into a NAND gate. The output of those gates and C go into an AND gate, giving Q, the output
So the expression is Q = (A NAND B) AND C
The truth table should have eight rows, and two output columns: one for the NAND, one for Q.
THE CIRCUIT ON YOUR NOTES

## Slide 14
THE CIRCUIT ON YOUR NOTES
A | B | C | A NAND B | Q
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 15
-> Notes Q3 [4 marks] - complete the eight-row table
Then, let’s check our answers together
YOUR TURN

## Slide 16
The exam usually describes a situation and asks you to build the logic yourself.
Three steps to do this:
Name each input with a letter and say what 1 means
Turn the sentence into an expression using and, or, not (and other gates if needed)
Build the table from the expression
FROM WORDS TO LOGIC

## Slide 17
A fan turns on when the temperature is high (T = 1) or the humidity is high (H = 1), but only when the system is switched on (S = 1).
Inputs: T, H, S. Output: F.
F = (T OR H) AND S
Make sure you’re paying attention to the logical order, that’s why we group the T and H, but the S is separate
  It can be difficult to devise where these things should be split up
THE FAN

## Slide 18
-> Notes Q4 (a)-(b)
Q4 (a) Write the Boolean expression for F. [1]
Q4 (b) Complete the eight-row truth table for F. [2]
THE FAN TABLE

## Slide 19
A Boolean expression and a logic diagram both represent Boolean logic, just in two different forms
  You are expected to know both for the exams
Brackets in the expression mean the logic gates must come first in the logic diagram
Each operator is one gate, a one to one relationship
EXPRESSIONS AND DIAGRAMS

## Slide 20
Q = (A AND B) OR (NOT C)
  Three operators, so three gates:
  A and B into an AND gate
  C into a NOT gate
  both of those outputs into an OR gate, giving Q
Use paper or an expo marker, and get a picture
DRAWING ONE

## Slide 21
-> Notes Q5 (a)-(c)
Q5 (a) Draw the logic diagram for Q = (A AND B) OR (NOT C). [2]
Q5 (b) Write the Boolean expression for the circuit in Q3. [1]
Q5 (c) State the difference between the standard symbols for AND and NAND. [1]
DIAGRAMS ON YOUR NOTES

## Slide 22
Gates cost money, power and space, so a circuit that does the same job with fewer gates is a better circuit. Boolean algebra is how you find it.
Here are some ways to simplify logic expressions
A AND A = A A OR A = A
A AND 1 = A A OR 0 = A
A AND 0 = 0 A OR 1 = 1
A AND NOT A = 0 A OR NOT A = 1
NOT(NOT A) = A
De Morgan's laws: NOT(A AND B) = NOT A OR NOT B
BOOLEAN ALGEBRA

## Slide 23
Q = (A AND B) OR (A AND NOT B)
B is 1 in the first term and 0 in the second, so between them they cover every value of B.
B cannot change the answer at all. Q = A.
So, we’ve gone from three gates to literally none
You can always check a simplification using a truth table
SIMPLIFYING, WORKED
A | B | NOT B | A AND NOT B | A AND B | Q
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1 | 1

## Slide 24
-> Notes Q6 (a)-(d)
Q6 (a) Simplify A AND (A OR B). [1]
Q6 (b) Simplify (A AND B) OR (A AND NOT B). [1]
Q6 (c) Simplify NOT(NOT A). [1]
Q6 (d) A circuit computes (A OR B) AND (A OR B). State how many gates can be removed, and why. [1]
SIMPLIFYING ON YOUR NOTES

## Slide 25
Algebra works, but only if you spot how to simplify it
  A Karnaugh map finds the same answer visually
  It is the truth table redrawn as a grid, with the columns in the order 00, 01, 11, 10
Neighboring cells differ by exactly one bit, so anything you can group is something that bit cannot affect
KARNAUGH MAPS
A\BC | 00 | 01 | 11 | 10
0 |  |  |  | 
1 |  |  |  | 

## Slide 26
Copy each 1 from the truth table into its cell, then circle groups of 1s.
Groups must be rectangles of 1, 2, 4 or 8 cells
  Bigger groups are better. Groups may overlap, and the edges can wrap around
Read each group by keeping the variables that stay the same and dropping the ones that change
GROUPING
A | B | C | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A\BC | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1

## Slide 27
Hmmm… y’know what…. it kind looks like only the value of B matters here, doesn’t it?
GROUPING
A | B | C | Q
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A\BC | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1

## Slide 28
-> Notes Q7 (a)-(c) [4 marks] - do them now
Q7 (a) Complete the Karnaugh map from the truth table given. [2]
Q7 (b) Circle the largest group and write the simplified expression. [1]
Q7 (c) State one advantage of a Karnaugh map over algebraic simplification. [1]
K-MAPS ON YOUR NOTES

## Slide 29
-> Notes Q8, Q9 and Q10
Q8 State the Boolean operator that outputs 1 only when its two inputs are different. [1]
Q9 Construct a truth table for Q = NOT A OR (B AND C). [3]
Q10 A door opens when a valid card is presented (C = 1) and either the manager is present (M = 1) or it is within opening hours (H = 1). Write the expression and draw the diagram. [4]
LAB

## Slide 30
Q8 XOR
Q9 Q = 1 1 1 1 0 0 0 1 reading down from A=0,B=0,C=0. Only the three rows where A is 1 and B AND C is 0 give 0
Q10 D = C AND (M OR H). One OR gate taking M and H, its output and C into an AND gate. Brackets, or the door opens on the manager alone
LAB ANSWERS

## Slide 31
WS A1-2: DIAGRAM DOUBLE DOWN
Five sections: name the gate, build tables, draw diagrams, simplify, and one Karnaugh map.

## Slide 32
Logic gate
Boolean operator
Truth table
Logic diagram
Boolean expression
AND / OR / NOT
NAND / NOR
VOCABULARY TO REMEMBER
XOR / XNOR
Inverter
Boolean algebra
De Morgan's laws
Karnaugh map
Grouping
Redundant gate